## Slide 1
House of Resistance - Centrifugals
track 2C

## Slide 2
House of Resistance - Centrifugals
and Jets
virtual training
2025

## Slide 3
gpm
Lift
Elevation
___ ft.
___ ft.
___
5
Pressure
___ psi
Friction
___ psi (loss)
things to know to select a pump
How it works is simple…
fill in five blanks.
explanation will be provided for each topic in the house, as the blanks get filled-in.

## Slide 4
gallons per minute
Represents the maximum flow rate (gpm) required of the pump.
Pump will be sized to the zone(s) that have the greatest demand for water in gpm.

## Slide 5
Zone 4
Home Water System
Fixture Count Method
The total number of fixtures in the house should equal the gpm rating of the pump.
Kitchen
● Sink
● Dishwasher
Laundry Room
● Clothes Washer
Full Bath
● Tub/Shower
● Lavatory
● Toilet
½ Bath
● Lavatory
● Toilet
● Outside Hose Bibb
2
1
2
3
+___
1
fixtures
9
9
9
gpm
9

## Slide 6
Zone 2
Zone 1
Zone 3
Zone 4
Zone 5
Rotors rated at 3 gpm
15 gpm Maximum Flow Rate
(5 x 3gpm)

## Slide 7
Pressure (psi)
Represents the maximum pressure (psi) required of the pump.
Irrigation
home water systems
50psi - 65psi
20psi - 45psi
15
45

## Slide 8
5 ft.
25 ft.
Elevation – from pump to highest
point in the system
Lift – from pump to
water source
Lift & Elevation
15
5
25
Pressure
___ psi
45
Friction
___ psi (loss)
Both expressed as feet.
Vertical Distances Only

## Slide 9
Friction (psi loss)
15
5
25
45
Occurs anytime two surfaces pass by one another.
Use Friction Loss Charts to determine (psi loss)

## Slide 10
How to read a Friction Loss chart
Pipe Length
Pipe Type
Pipe Size
what you need to know
PVC/SCH 40
PVC/SCH 80
PVC/SCH 120
POLY
SDR-21
SDR-26
SCH 40 Steel
50’
100’
150’
200’
250’
300’
350’
400’
500’
0.50”
0.75”
1.00”
1.25”
1.50”
2.00”
3.00”
4.00”
Flow Rate
(gpm)
15 gpm

## Slide 11
Pipe Type
Pipe Size
Flow Rate
(gpm)
Lose 0.68 psi / 100 ft
Lose 2 psi / 300 ft
Pressure
(psi loss)
15 gpm flowing through 1.50” pipe, will lose 0.68 psi per 100’ of pipe
Velocity
(feet/sec)
15 gpm flowing through 1.50” pipe, will move at a speed of 2.41 feet per second, per 100’ of pipe
Friction Loss
2 psi

## Slide 12
15
5
25
45
Zone 4 7 Rotors
Zone 5 3 Rotors
Friction Loss
2 psi
Friction (psi loss)
2

## Slide 13
15
5
25
45
2
Zone 5 3 Rotors
Convert Pressure (psi) to Feet (ft)
x 2.31=
Pressure
Friction
x 2.31
x 2.31
psi (loss)
45
2
psi
103.95
4.62
____ ft.
____ ft.
104
5
why is 2.31 the multiplier?

## Slide 14
Zone 5 3 Rotors
Convert Pressure (psi) to Feet (ft)
x 2.31=
15
5
25
104
5
1 ft
2 ft
3 ft
2.31 feet
1 psi
1 psi = 2.31 ft.
to convert feet to psi
x .433
(104 x .433 = 45.02 psi)
____ feet x .433 = psi

## Slide 15
15
5
25
104
5
Zone 4 7 Rotors
Zone 5 3 Rotors
House contains resistance that pump must overcome
all blanks are filled-in

## Slide 16
15
5
25
104
5
Zone 4 7 Rotors
Zone 5 3 Rotors
Time to total-up the house
Pressure 104
Lift 5
Elevation 25
Friction 5
+ ___
139 feet

## Slide 17
These two numbers
139 feet
15
gpm
___
we can look at a pump curve and select a pump
Referred to as
Total Dynamic Head (TDH)

## Slide 18
How to read a pump curve
At 139 feet
5 gpm
16 gpm
23 gpm
32 gpm
40 gpm
1½ hp 2-stage

## Slide 19
25
8
18
116
8
Zone 4 7 Rotors
Zone 5 3 Rotors
Time to total-up the house
Pressure 116
Lift 8
Elevation 18
Friction 8
+ ___
150 feet
8 Rotors
50 psi

## Slide 20
These two numbers
150 feet
gpm
25
___
At 150 feet
4 gpm
12 gpm
31 gpm
34 gpm
2 hp 3-stage

## Slide 21
https://www.youtube.com/@flintandwalling
track 2B
subscribe