## Slide 1
Winterizing Above Ground Pumps

## Slide 2
Water
weighs 8.34 lbs./gallon
Liquid (friend) Solid (foe)
water
8.34 lbs.
ice
8.34 lbs.
FREEZING WATER IN A CONFINED SPACE CAN EXERT UP TO
30,000 PSI

## Slide 3
CAST IRON - has more strength than steel. It’s high hardness,
wear resistance and compressive strength makes
it ideal for pump housings, machine parts and
even engine blocks.

## Slide 4
STEEL - on the other hand…steel has more tensile strength than
cast iron, which allows it to bend without necessarily
breaking.
To clarify, compressive strength makes iron very hard,
resistant to bending. On the downside, low tensile
strength causes cracking under excessive pressure.

## Slide 5
CAST IRON, while extremely strong, is
especially susceptible to freeze
damaged caused by water
expanding as it turns to ice. This
excessive pressure combined
with the contraction of cast iron
in cold weather leads to cracked
pump housings.

## Slide 8
Centrifugals
Self-Primers
Jets
Winterizing Above Ground Pumps
Irrigation
Home

## Slide 9
Centrifugals
Self-Primers
Jets
Winterizing Above Ground Pumps
5 common methods

## Slide 10
° Drain
° Blow-out
° Antifreeze
° Heat
° Removal
5 common methods

## Slide 11
° Drain the pump
Step One Turn off power to the pump

## Slide 12
Step Two Open a valve or faucet to drain water from piping & tank
° Drain the pump

## Slide 13
Step Three Remove drain plug(s) on the bottom of the pump
° Drain the pump

## Slide 14
° Drain the pump

## Slide 15
° Drain the pump

## Slide 16
° Drain the pump
DOWNSIDE: Nearly impossible to get all the water out of the pump

## Slide 17
° Drain the pump

## Slide 18
Hey guys, I have a contractor who purchased 2 of these last year. Both were drained and winterized.
He is trying
to figure how they could have
split and if there is any
help he could get to get them
replaced, fixed etc.
appreciate any feedback.
Thanks,

## Slide 19
° Blow-out
Complete previous Steps 1-3
Use compressed air to blow-out the
pump body.

## Slide 20
° Blow-out
Set compressor to safe level, typically between 40-80 psi.

## Slide 21
Set compressor to safe level, typically between 40-80 psi.
Allow the compressor to run until you see a fog or mist coming out of the pump.
° Blow-out

## Slide 22
° Antifreeze
Complete previous Steps 1-3
Fill the pump with antifreeze

## Slide 23
° Antifreeze
FOOD GRADE PROPYLENE GLYCOL

## Slide 24
° Antifreeze
OFTEN MIXED WITH WATER

## Slide 25
° Antifreeze
SHOULD NEVER BE CONFUSED WIT AUTOMOTIVE ANTIFREEZE USED IN RADIATORS WHICH IS CALLED ETHYLENE GLYCOL
FOOD GRADE PROPYLENE GLYCOL

## Slide 26
° Heat
Wrap pump and external piping with heat tape.
Heat lamp – thermostat controlled.

## Slide 27
° Remove
Remove pump and store in a heated area.
100% GUARANTEE!

## Slide 28
Drain
Blow-out
Antifreeze
Heat
Removal
5 common methods
GOOD
BETTER
BEST

## Slide 29
Average winter temperatures (F°) by state

## Slide 30
https://www.youtube.com/@flintandwalling
track 2B
subscribe